## Slide 1: DP1. Migration 실행 구조 (Executor 이후) - 설계
Migration 실행 · Location commit · Inference engine 위치 통지
Q1
Q2
C2
F1
C1
(When, What,
Where to locate?)
설계 안 | DP1 결정 → 공통 Migration subsystem (WHAT/WHERE는 DP1, HOW/WHEN/COMMIT은 Migration subsystem)
구조 | 
“Policy decides WHAT and WHERE. Migration subsystem decides HOW, WHEN, and COMMIT“
Decision Plane (DP1, 기존)
Migration Control Plane - EngineCore process (신규·공통)
Transfer Data Plane - Worker process
Migration Data
Selector
Migration Executor
(DP1 출구 boundary:
결정만 넘기고 복사는 안 함)
MigrationIntent
object id (logical)
source tier → target tier
action: MOVE · REPLICATE ·
DROP · REMAP · RECLASSIFY
reason · priority
(foreground / background)
① MigrationCoordinator Intent 수신·검증, job lifecycle 관리
③ Data
Location
Store
logical id →
physical location
(resource,
alloc, offset,
version)
copy 중에는
source가
authoritative
⑨ commit 시에만
target으로 전환
(version+1)
② KVDataAdapter
can_migrate_now (sealed?)
source pin / 이동 중 free 금지
④ MigrationPlanner
target reserve (MemoryResourceRegistry)
path: direct / staged / multi-hop
⑤ MigrationScheduler
foreground(blocking) 우선, background는 link 몫 내
⑥ SchedulerOutput (step boundary 공유)
migration_commands[ job, transfer_steps, src/dst spec ] + migration_dependencies[ request, job_ids, wait_before=MODEL_FORWARD ]
⑧⑨ CompletionReconciler version·source 유효 검증 → atomic commit(location=target, version+1) → source 해제·unpin
Worker = copy executor
위치 결정·commit 권한 없음
(logical migration authority는 EngineCore)
Job 상태 (EngineCore가 관리)
PENDING → PREPARING → COPYING
→ VERIFYING → COMMITTING → COMPLETED
실패·stale·worker crash
→ target 폐기, source authoritative 유지
→ 재계획 (rollback)
MigrationExecutor (Worker)
Command batch 수신, 비동기 handle 발급
⑦ TransferRouter → TransferHandler
CUDA P2P · Host DMA · CXL · NVMe 중 선택, source 유지한 채 target에 쓰기
HBM · ScHBM · CXL-PNM · DRAM · HBF · SSD-PIM 사이 (Phase 1: 기존 OffloadingWorker 재사용)
Inference engine에 물리 위치를 알리는 경로 (logical block id는 그대로, 위치만 교체)
색: 파랑=DP1 기존 · 주황=신규(공통 migration) · 초록=기존 vLLM 수정 · 회색=재사용
⑨ commit 결과
logical id → 새 physical location (resource, alloc, offset, version+1). 이전 HBM block unpin·release
KVCacheManager / BlockPool
Scheduler는 logical block id만 봄. 위치는 KVDataAdapter가 DataLocationStore에서 조회
다음 step: Scheduler.schedule()
필요 KV가 하위 tier면 foreground promotion job + dependency를 SchedulerOutput에 실음
Worker: dependency 대기
migration job 완료까지 MODEL_FORWARD 진입 전 wait (Phase 1: forward 앞 barrier)
GPUModelRunner.execute_model()
required KV가 HBM의 새 physical block에 있음 → attention 수행
핵심: copy 중엔 source가 authoritative, 검증 후에만 atomic commit, 새 위치는 다음 step의 SchedulerOutput으로 전달 (설계 단계, 미구현)
Notes: C2의 runtime state monitor에 대한 설명
“Data type label만 가지고 배치한 것이 아니라, object별 access event를 online으로 수집하고 access-rate EWMA, inter-access interval, idle duration, object age를 관리했습니다. Cold start에서는 data-class prior를 사용하고 observation이 축적되면 prior weight를 exponential decay시켜 실제 runtime behavior가 prediction을 지배하도록 했습니다.”